## Slide 1: Module 11: Switch Security Configuration
Switching, Routing and Wireless Essentials v7.0 (SRWE)
Notes: Cisco Networking Academy Program
Switching, Routing and Wireless Essentials v7.0 (SRWE)
Module 11: Switch Security Configuration

## Slide 2: Module Objectives
Module Title: Switch Security Configuration
Module Objective: Configure switch security to mitigate LAN attacks
Topic Title | Topic Objective
Implement Port Security | Implement port security to mitigate MAC address table attacks.
Mitigate VLAN Attacks | Explain how to configure DTP and native VLAN to mitigate VLAN attacks.
Mitigate DHCP Attacks | Explain how to configure DHCP snooping to mitigate DHCP attacks.
Mitigate ARP Attacks | Explain how to configure ARP inspection to mitigate ARP attacks.
Mitigate STP Attacks | Explain how to configure PortFast and BPDU Guard to mitigate STP Attacks.
Notes: 2
11- Switch Security Configuration
11.0- Introduction
11.0.2 – What will I learn in this module?

## Slide 3: 11.1 Implement Port Security
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security

## Slide 4: Implement Port Security Secure Unused Ports
Layer 2 attacks are some of the easiest for hackers to deploy but these threats can also be mitigated with some common Layer 2 solutions.
All switch ports (interfaces) should be secured before the switch is deployed for production use. How a port is secured depends on its function.
A simple method that many administrators use to help secure the network from unauthorized access is to disable all unused ports on a switch. Navigate to each unused port and issue the Cisco IOS shutdown command. If a port must be reactivated at a later time, it can be enabled with the no shutdown command.
To configure a range of ports, use the interface range command.
Switch(config)# interface range type module/first-number – last-number
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.1 – Secure Unused Ports

## Slide 5: Implement Port Security Mitigate MAC Address Table Attacks
The simplest and most effective method to prevent MAC address table overflow attacks is to enable port security.
Port security limits the number of valid MAC addresses allowed on a port. It allows an administrator to manually configure MAC addresses for a port or to permit the switch to dynamically learn a limited number of MAC addresses. When a port configured with port security receives a frame, the source MAC address of the frame is compared to the list of secure source MAC addresses that were manually configured or dynamically learned on the port.
By limiting the number of permitted MAC addresses on a port to one, port security can be used to control unauthorized access to the network.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.2 – Mitigate MAC Address Table Attacks

## Slide 6: Implement Port Security Enable Port Security
Port security is enabled with the switchport port-security interface configuration command.
Notice in the example, the switchport port-security command was rejected. This is because port security can only be configured on manually configured access ports or manually configured trunk ports. By default, Layer 2 switch ports are set to dynamic auto (trunking on). Therefore, in the example, the port is configured with the switchport mode access interface configuration command.
Note: Trunk port security is beyond the scope of this course.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.3 – Enable Port Security

## Slide 7: Implement Port Security Enable Port Security (Cont.)
Use the show port-security interface command to display the current port security settings for FastEthernet 0/1.
Notice how port security is enabled, the violation mode is shutdown, and how the maximum number of MAC addresses is 1.
If a device is connected to the port, the switch will automatically add the device’s MAC address as a secure MAC. In this example, no device is connected to the port.
Note: If an active port is configured with the switchport port-security command and more than one device is connected to that port, the port will transition to the error-disabled state.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.3 – Enable Port Security (Cont.)

## Slide 8: Implement Port Security Enable Port Security (Cont.)
After port security is enabled, other port security specifics can be configured, as shown in the example.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.3 – Enable Port Security (Cont.)

## Slide 9: Implement Port Security Limit and Learn MAC Addresses
To set the maximum number of MAC addresses allowed on a port, use the following command:
The default port security value is 1.
The maximum number of secure MAC addresses that can be configured depends the switch and the IOS.
In this example, the maximum is 8192.
Switch(config-if)# switchport port-security maximum value
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.4 – Limit and Learn MAC Addresses

## Slide 10: Implement Port Security Limit and Learn MAC Addresses (Cont.)
The switch can be configured to learn about MAC addresses on a secure port in one of three ways:
1. Manually Configured: The administrator manually configures a static MAC address(es) by using the following command for each secure MAC address on the port:
Switch(config-if)# switchport port-security mac-address mac-address
2. Dynamically Learned: When the switchport port-security command is entered, the current source MAC for the device connected to the port is automatically secured but is not added to the running configuration. If the switch is rebooted, the port will have to re-learn the device’s MAC address.
3. Dynamically Learned – Sticky: The administrator can enable the switch to dynamically learn the MAC address and “stick” them to the running configuration by using the following command:
Switch(config-if)# switchport port-security mac-address sticky
Saving the running configuration will commit the dynamically learned MAC address to NVRAM.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.4 – Limit and Learn MAC Addresses (Cont.)

## Slide 11: Implement Port Security Limit and Learn MAC Addresses (Cont.)
The example demonstrates a complete port security configuration for FastEthernet 0/1.
The administrator specifies a maximum of 4 MAC addresses, manually configures one secure MAC address, and then configures the port to dynamically learn additional secure MAC addresses up to the 4 secure MAC address maximum.
Use the show port-security interface and the show port-security address command to verify the configuration.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.4 – Limit and Learn MAC Addresses (Cont.)

## Slide 12: Implement Port Security Port Security Aging
Port security aging can be used to set the aging time for static and dynamic secure addresses on a port and two types of aging are supported per port:
  Absolute - The secure addresses on the port are deleted after the specified aging time.
  Inactivity - The secure addresses on the port are deleted if they are inactive for a specified time.
Use aging to remove secure MAC addresses on a secure port without manually deleting the existing secure MAC addresses.
Aging of statically configured secure addresses can be enabled or disabled on a per-port basis.
Use the switchport port-security aging command to enable or disable static aging for the secure port, or to set the aging time or type.
Switch(config-if)# switchport port-security aging {static | time time | type {absolute | inactivity}}
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.5 – Port Security Aging

## Slide 13: Implement Port Security Port Security Aging (Cont.)
The example shows an administrator configuring the aging type to 10 minutes of inactivity.
The show port-security command confirms the changes. interface command to verify the configuration.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.5 – Port Security Aging (Cont.)

## Slide 14: Implement Port Security Port Security Violation Modes
If the MAC address of a device attached to a port differs from the list of secure addresses, then a port violation occurs and the port enters the error-disabled state.
To set the port security violation mode, use the following command:
Switch(config-if)# switchport port-security violation {shutdown | restrict | protect}
Mode | Description
shutdown (default) | The port transitions to the error-disabled state immediately, turns off the port LED, and sends a syslog message. It increments the violation counter. When a secure port is in the error-disabled state, an administrator must re-enable it by entering the shutdown and no shutdown commands.
restrict | The port drops packets with unknown source addresses until you remove a sufficient number of secure MAC addresses to drop below the maximum value or increase the maximum value. This mode causes the Security Violation counter to increment and generates a syslog message.
protect | This is the least secure of the security violation modes. The port drops packets with unknown MAC source addresses until you remove a sufficient number of secure MAC addresses to drop below the maximum value or increase the maximum value. No syslog message is sent.
The following table shows how a switch reacts based on the configured violation mode.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.6 – Port Security Violation Modes

## Slide 15: Implement Port Security Port Security Violation Modes (Cont.)
The example shows an administrator changing the security violation to “Restrict”.
The output of the show port-security interface command confirms that the change has been made.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.6 – Port Security Violation Modes (Cont.)

## Slide 16: Implement Port Security Ports in error-disabled State
When a port is shutdown and placed in the error-disabled state, no traffic is sent or received on that port.
A series of port security related messages display on the console, as shown in the following example.
Note: The port protocol and link status are changed to down and the port LED is turned off.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.7 – Ports in error-disabled State

## Slide 17: Implement Port Security Ports in error-disabled State (Cont.)
In the example, the show interface command identifies the port status as err-disabled. The output of the show port-security interface command now shows the port status as secure-shutdown. The Security Violation counter increments by 1.
The administrator should determine what caused the security violation If an unauthorized device is connected to a secure port, the security threat is eliminated before re-enabling the port.
To re-enable the port, first use the shutdown command, then, use the no shutdown command.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.7 – Ports in error-disabled State (Cont.)

## Slide 18: Implement Port Security Verify Port Security
After configuring port security on a switch, check each interface to verify that the port security is set correctly, and check to ensure that the static MAC addresses have been configured correctly.
To display port security settings for the switch, use the show port-security command.
The example indicates that all 24 interfaces are configured with the switchport port-security command because the maximum allowed is 1 and the violation mode is shutdown.
No devices are connected, therefore, the CurrentAddr (Count) is 0 for each interface.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.8 – Verify Port Security

## Slide 19: Implement Port Security Verify Port Security (Cont.)
Use the show port-security interface command to view details for a specific interface, as shown previously and in this example.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.8 – Verify Port Security (Cont.)

## Slide 20: Implement Port Security Verify Port Security (Cont.)
To verify that MAC addresses are “sticking” to the configuration, use the show run command as shown in the example for FastEthernet 0/19.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.8 – Verify Port Security (Cont.)

## Slide 21: Implement Port Security Verify Port Security (Cont.)
To display all secure MAC addresses that are manually configured or dynamically learned on all switch interfaces, use the show port-security address command as shown in the example.
Notes: 11 – Switch Security Configuration
11.1 – Implement Port Security
11.1.8 – Verify Port Security (Cont.)
11.1.9 – Syntax Checker – Implement Port Security

## Slide 22: 11.3 Mitigate DHCP Attacks
Notes: 11 – Switch Security Configuration
11.3 - Mitigate DHCP Attacks

## Slide 23: Mitigate DHCP Attacks DHCP Attack Review
The goal of a DHCP starvation attack is to an attack tool such as Gobbler to create a Denial of Service (DoS) for connecting clients.
Recall that DHCP starvation attacks can be effectively mitigated by using port security because Gobbler uses a unique source MAC address for each DHCP request sent. However, mitigating DHCP spoofing attacks requires more protection.
Gobbler could be configured to use the actual interface MAC address as the source Ethernet address, but specify a different Ethernet address in the DHCP payload. This would render port security ineffective because the source MAC address would be legitimate.
DHCP spoofing attacks can be mitigated by using DHCP snooping on trusted ports.
Notes: 11 – Switch Security Configuration
11.3 - Mitigate DHCP Attacks
11.3.1 – DHCP Attack Review

## Slide 24: Mitigate DHCP Attacks DHCP Snooping
DHCP snooping filters DHCP messages and rate-limits DHCP traffic on untrusted ports.
Devices under administrative control (e.g., switches, routers, and servers) are trusted sources.
Trusted interfaces (e.g., trunk links, server ports) must be explicitly configured as trusted.
Devices outside the network and all access ports are generally treated as untrusted sources.
A DHCP table is built that includes the source MAC address of a device on an untrusted port and the IP address assigned by the DHCP server to that device.
The MAC address and IP address are bound together.
Therefore, this table is called the DHCP snooping binding table.
Notes: 11 – Switch Security Configuration
11.3 - Mitigate DHCP Attacks
11.3.2 – DHCP Snooping

## Slide 25: Mitigate DHCP Attacks Steps to Implement DHCP Snooping
Use the following steps to enable DHCP snooping:
  Step 1. Enable DHCP snooping by using the ip dhcp snooping global configuration command.
  Step 2. On trusted ports, use the ip dhcp snooping trust interface configuration command.
  Step 3: On untrusted interfaces, limit the number of DHCP discovery messages that can be received using the ip dhcp snooping limit rate packets-per-second interface configuration command.
  Step 4. Enable DHCP snooping by VLAN, or by a range of VLANs, by using the ip dhcp snooping vlan global configuration command.
Notes: 11 – Switch Security Configuration
11.3 - Mitigate DHCP Attacks
11.3.3 – Steps to Implement DHCP Snooping

## Slide 26: Mitigate DHCP Attacks DHCP Snooping Configuration Example
Refer to the DHCP snooping sample topology with trusted and untrusted ports.
DHCP snooping is first enabled on S1.
The upstream interface to the DHCP server is explicitly trusted.
F0/5 to F0/24 are untrusted and are, therefore, rate limited to six packets per second.
Finally, DHCP snooping is enabled on VLANS 5, 10, 50, 51, and 52.
Notes: 11 – Switch Security Configuration
11.3 - Mitigate DHCP Attacks
11.3.4 - DHCP Snooping Configuration Example

## Slide 27: Mitigate DHCP Attacks DHCP Snooping Configuration Example (Cont.)
Use the show ip dhcp snooping privileged EXEC command to verify DHCP snooping settings.
Use the show ip dhcp snooping binding command to view the clients that have received DHCP information.
Note: DHCP snooping is also required by Dynamic ARP Inspection (DAI).
Notes: 11 – Switch Security Configuration
11.3 - Mitigate DHCP Attacks
11.3.4 - DHCP Snooping Configuration Example (Cont.)
11.3.5 – Syntax Checker – Mitigate DHCP Attacks